Methodological approach

Different wind speed
Firstly we compared wind history 1 and 4 in dry conditions: these ones present the same turbulence intensity but different wind speed as can be seen in the table. We decided to focus on aerodynamic forces and moment (on your left) and the trajectory of the vehicle. As can be seen from the plots, the trends of the aerodynamic forces and moment are quite the same and do not change as much as the modulus does. Moreover, as expected the trajectory plot in the second case shows that the vehicle is more unbalanced due to the higher velocity

Different turbulence intensity
Now we compared wind history 1 and 4 which have the same wind speed and different turbulence intensity. As can be seen from the wind yaw angle and speed the frequency content is more distributed at high frequencies, which is why the average value of the quantities is similar in the two cases, while the peaks are clearly different. From the plot Loads on the Wheels on right, can be noticed that the peaks are more relevant and the modulus change considerably in the second case over time.

Different meteorological conditions
Here we compared different weather conditions taking in account wind history 5. As can be seen the main variations occur when snow condition is considered. In fact the trajectory has a deviation from 0 of 1.2-1.8 compared to 0.2 of dry and wet cases.
The steer angle plot shows that the driver is trying to go against the effect of the wind force and there’s a peak of 27 °.
The vehicle is much faster in the snow case, with a peak speed of 35 km/h, compared to the dry and wet cases

Load variation

Roll stiffness variation

# Lane change
In the last part of the presentation we analyzed the behaviour of the truck considering different paths: in the first case, we considered a change of the lane, while in the second and last case an entrance and exiting from a tunnel. For the lane change, we performed the simulation changing the referencepath, which is no more a straight line but the position of the y direction changes. In this slide are reported the trajectory, the steer angle and the load on wheels considering wind history 6 and comparing the results for without the lane change. In the trajectory the change in y direction is highlighted, and the change in the wheels direction is visible also in the steer angle: we recognize the four instants when the driver turns the steering wheel and performs the maneuver. However, differently from the previous analyses, the effect on the vertical load on the wheels is not appreciable.
# Tunnel
In the end we considered a different situation: the truck enters and exits from a tunnel. This simulation is performed putting the wind speed equal to 0.4 m/s form 20 to 40 seconds in all positions (it is not strictly equal to 0 to avoid numerical errors). Here are reported the wind speed, the trajectory, the roll angle and the loads on the wheels, for both conditions with and without the tunnel. When the truck gets into the tunnel, the wind stops pushing the truck and the driver starts recovering the desired path, which is a straight line. In the roll angle figure we can appreciate the little transient when the truck still rolls even if there is no more wind. The same effect is visible also in the load on wheels figure. When the truck exits from the tunnel, the condition is similar to the case without the gallery, and after a certain time the diffreence between the two simulations are no more appreciable.